## Slide 1: Predict the fuel burnt (kg)
PRC Data Challenge 2025
October 2025
Team details:
Your team name is: understated-zucchini
Your submission bucket is : prc-2025-understated-zucchini

## Slide 2: Main principle
Feed the model with Fuel Flow Kg/Seconds (instead of fuel Kilograms)
Compute the Fuel Flow from Fuel (kg) between Fuel Start Instant and Fuel End Instant
  Assert that End Instant is greater than Start Instant

## Slide 3: Principles
Read Fuel Train records
  compute time difference seconds = fuel record end – fuel record start
  Compute fuel flow kg per seconds = fuel kg / ( fuel record end – fuel record start )
Link to Flight List using the flight id
  Compute fuel burn relative start = fuel burnt start – takeoff (from the related flight list)
  Compute fuel burn relative end = fuel burnt end – takeoff (from the related flight list)
Extend fuel records with attributes coming from the flight list
  Add origin longitude, origin latitude, origin_elevation
  Add destination longitude, destination latitude, destination elevation
  Add flight distance Nautical Miles and flight duration seconds

## Slide 4: Data Model
Fuel Data
Flight Data
Flight id
TimeStamp relative start
Flight List Data
Airport Data
Aircraft Data
Flight id
origin airport ICAO code
destination airport ICAO code
Aircraft ICAO code

## Slide 5: Airports data sanity checks from airports.parquet
Airport ZGOW Jieyang Chaoshan International Airport has a missing “elevation ft”
Status as of

## Slide 6: Airports data sanity checks
Icao code not empty and length > 0
Latitude in the range -90,0 and + 90,0
Longitude in the range -180 and +180,0
Elevation in feet > 0,0 feet
Elevation in feet * feet_to_meters < 5000,0 meters
Notes:
  airport ICAO = ZUDR --> elevation = 14108.0 feet--> elevation = 4300.1184 meters
  airport ICAO = ZX and UPL --> elevation = 13943.0 feet --> elevation = 4249.8264 meters

## Slide 7: Airports data sanity checks
airport ICAO = LLMZ --> elevation (feet) = -1266.0 --> elevation meters = -385.8768

## Slide 8: Flight list records – sanity checks
Assert (takeoff() != null )
Assert (takeoff().getEpochSecond() > 0)
Assert (landed() != null)
Asser (landed().getEpochSecond() > 0)
Assert landed().isAfter(takeoff())
Example for Java code

## Slide 9: Set takeoff and landing date type as UTC Compute flight distance compute flight duration Extract year from takeoff Extract month from takeoff Extract day of the year (1..365) from takeoff Compute distance (great circle using haversine method) between departure and arrival airports compute flight duration between takeoff and landing -> Principles is to get rid of absolute datetime convert lat long into sine and cosine -> favorize model analysis because of discontinuity from -180 degrees to 0 degrees and avoid scaling only absolute degrees
Extend Flight list records

## Slide 10: Extend flight list data
Suppress airport names
Compute distance (Nautical miles) between departure and arrival airport
Convert all Date Time instant to UTC
Compute flight time between flight takeoff and flight landed
Use time difference for all instant versus flight takeoff
From flight date
  extract year and month
  Compute day number in the current year (range 1 to 365)
Suppress absolute dates as they are replaced by relative ones from takeoff instant

## Slide 11: Check great circle distance (in nautical miles)
origin_icao | origin_name | destination_icao | destination_name | flight_distance_Nautical miles
MMGL | Guadalajara International Airport | KOAK | Oakland International Airport | 1427.58
Oakland
Guadalajara

## Slide 12: Feature engineering of fuel absolute datetime instant
Compute relative duration in seconds from the “flight” takeoff instant
Fuel Start Instant (UTC) -> converted to duration from the “takeoff”UTC Instant
Fuel End Instant (UTC) – converted to duration from the “takeoff” UTC Instant

## Slide 13: Feature engineering heading-track-and-radial
Heading. The direction in which the longitudinal axis of an aircraft is pointed, usually expressed in degrees from North (true, magnetic, compass or grid). (Source: ICAO)
Track. The projection on the earth’s surface of the path of an aircraft, the direction of which path at any point is usually expressed in degrees from North (true, magnetic or grid). (Source: ICAO)
Radial. A magnetic bearing extending from a VOR/VORTAC/TACAN. (Source: UK CAA)
Bearing. The horizontal direction to or from any point, usually measured clockwise from true north, magnetic north, or some other reference point through 360 degrees. (Source: US FAA)

## Slide 14: Feature engineering of track angles
The track angle is given in Decimal degrees
Angles in the range 0 degrees to 360 degrees are not good inputs to the models
Because 360° et 0° must be near and avoid discontinuity when moving from 360 degrees to 0 degrees.
To avoid discontinuity
Compute sinus and cosinus of each angles
In radians before feeding the model
For the track angle compute a vector
from the ground speed

## Slide 15: Feature engineering of aircraft track angles and of any speed related to the track angle
Mais la donnée « aircraft track angle » sera plus facile à interpréter pour le modèle si vous convertissez les colonnes de direction et de vitesse de l’avion en un vecteur vitesse
import numpy as np
''' convert track angles from degrees to radians '''
track_radians = df.pop('track')* np.pi / 180
groundSpeedMax = df['groundspeed'].max()
groundSpeed = df.pop('groundspeed')
# Calculate the aircraft speed x and y components.
df['groundspeed_x'] = groundSpeed * np.cos(track_radians)
df['groundspeed_y'] = groundSpeed * np.sin(track_radians)

## Slide 16: airports lat/lon and aircraft lat/lon
Latitude:
Values range from -90° to +90°.
Lines of latitude run east-west and are parallel to each other.
The equator is at 0° latitude.
Longitude:
Values range from -180° to +180°.
Lines of longitude run north-south and converge at the poles.
The prime meridian (0° longitude) runs through Greenwich, England. These ranges define the geographic coordinate system used to specify locations on Earth.

## Slide 17: airports latitude and longitude versus aircraft flight position lat/lon
Translate each aircraft (interpolated position) at fuel start and fuel end
Use Latitude Longitude of interpolated aircraft position to compute
For each fuel start Instant
  Haversine distance Nm from aircraft position (lat/lon) to departure airport (lat/lon)
  Haversine distance Nm from aircraft position (lat/lon) to arrival airport (lat/lon)
For each fuel end Instant
  Haversine distance Nm from aircraft position (lat/lon) to departure airport (lat/lon)
  Haversine distance Nm from aircraft position (lat/lon) to arrival airport (lat/lon)

## Slide 18: Flight data cleaning
Example -> training flight prc770822360 contains duplicated timestamps
org.apache.commons.math3.exception.NonMonotonicSequenceException: les points 12 et 13 ne sont pas strictement croissants (1 744 474 640 >= 1 744 474 640)

## Slide 19: Aircrafts data
File obtained from FAA site
FAA-Aircraft-Char-DB-AC-150-5300-13B-App-2023-09-07.xlsx
Contains 2 interesting columns that may be signals for the fuel consumption
  Wingspan_ft_without_winglets_sharklets
  Wingspan_ft_with_winglets_sharklets

## Slide 20
Training versus validation loss

## Slide 21: Training versus Validation loss
16 october 2025
Y = fuel flow kg per seconds
Make the val_loss as low as possible
All train records
133984 train fuel records
11085 train flight files

## Slide 22: Do not
You do not need to scale the Y of train data as the algorithm or model will set the parameter values to get least Cost (error), that is k {Y (output)-Y (original)} anyway.

## Slide 23: 25 October 2025
Input to the modeling
Train-> ['time_diff_seconds', 'fuel_flow_kg_sec', 'aircraft_latitude_at_fuel_start', 'aircraft_longitude_at_fuel_start', 'aircraft_latitude_at_fuel_end', 'aircraft_longitude_at_fuel_end', 'aircraft_distance_flown_Nm', 'aircraft_altitude_ft_at_fuel_start', 'aircraft_altitude_ft_at_fuel_end', 'aircraft_computed_vertical_rate_ft_min', 'aircraft_groundspeed_kt_at_fuel_start', 'aircraft_groundspeed_kt_at_fuel_end', 'aircraft_track_angle_deg_at_fuel_start', 'aircraft_track_angle_deg_at_fuel_end', 'aircraft_vertical_rate_ft_min_at_fuel_start', 'aircraft_vertical_rate_ft_min_at_fuel_end', 'origin_elevation_feet', 'destination_elevation_feet', 'flight_distance_Nm', 'flight_duration_sec’]
Rank -> ['time_diff_seconds', 'aircraft_latitude_at_fuel_start', 'aircraft_longitude_at_fuel_start', 'aircraft_latitude_at_fuel_end', 'aircraft_longitude_at_fuel_end', 'aircraft_distance_flown_Nm', 'aircraft_altitude_ft_at_fuel_start', 'aircraft_altitude_ft_at_fuel_end', 'aircraft_computed_vertical_rate_ft_min', 'aircraft_groundspeed_kt_at_fuel_start', 'aircraft_groundspeed_kt_at_fuel_end', 'aircraft_track_angle_deg_at_fuel_start', 'aircraft_track_angle_deg_at_fuel_end', 'aircraft_vertical_rate_ft_min_at_fuel_start', 'aircraft_vertical_rate_ft_min_at_fuel_end', 'origin_elevation_feet', 'destination_elevation_feet', 'flight_distance_Nm', 'flight_duration_sec']

## Slide 24: missing
Date of the flight -> year, month, day in the year
Fuel burn relative start to takeoff
Fuel burn relative end to takeoff
Fuel burn relative end to landed
Mach
CAS
TAS
Aircrafts data

## Slide 25: steps
Read fuel records
Extend each fuel record with flight data
Scale and encode aircraft icao code
Read Flight list records
Extend fuel records with flight list data
Y column is fuel flow kg per seconds
Use fuel start end relative stamp to link with flight record timestamp
Timestamp inside start – end of fuel record
Compute fuel flow kg per seconds
Compute flight distance (Nm)
Compute flight duration (seconds)
Encode aircraft_icao_code
Scale all columns

## Slide 26: Flight file with issues
Parquet file <<C:\Users\rober\git\PRCdataChallenge2025\Data-Download-OpenSkyNetwork\competition-rank-data\prc806717600.parquet>

## Slide 27: Leveraging TensorFlow for Regression Problems: Techniques and Applications
Exploring tools and methods to improve regression modeling
Notes: AI-generated content may be incorrect. --- This presentation explores how TensorFlow can be effectively used to solve regression problems. We will cover foundational regression concepts, TensorFlow’s features, practical implementation of regression models, and advanced methods to enhance model performance. Image source: Microsoft 365 content library

## Slide 28: Presentation Agenda
Introduction to Regression Analysis
Overview of TensorFlow and Its Capabilities
Implementing Regression Models in TensorFlow
Advanced Techniques and Best Practices
Notes: --- We will begin with an introduction to regression analysis, its types and applications. Next, we will look at TensorFlow’s capabilities and setup. Then, practical steps to implement regression models using TensorFlow. Finally, advanced techniques and best practices for improving regression models. Image source: Microsoft 365 content library

## Slide 29: Introduction to Regression Analysis
Notes: Regression analysis is a key statistical method for modelling relationships between variables. Understanding its basic concepts, types, and real-world use cases lays the foundation for applying TensorFlow in regression tasks.

## Slide 30: Fundamental concepts of regression
Definition of Regression
  Regression estimates relationships between dependent and independent variables to understand their connection.
Predicting Continuous Outcomes
  The goal of regression is to predict continuous variables based on input data from other variables.
Understanding Variable Influence
  Regression helps identify how independent variables influence the dependent variable in a measurable way.
Notes: --- Regression involves estimating the relationship between dependent and independent variables. We aim to predict continuous outcomes and understand how variables influence each other. Image source: Microsoft 365 content library

## Slide 31: Types of regression problems
Linear Regression
  Linear regression models the relationship between variables using a straight line for simple, direct trends.
Polynomial Regression
  Polynomial regression handles complex data by fitting a curved line to capture non-linear relationships.
Logistic Regression
  Logistic regression models probabilities for classification problems using an S-shaped logistic curve.
Notes: --- Common regression types include linear, polynomial, and logistic regression. Each type addresses different data patterns and modelling needs, from simple linear relationships to complex non-linear dependencies. Image source: Microsoft 365 content library

## Slide 32: Overview of TensorFlow and Its Capabilities
Notes: TensorFlow is a powerful open-source framework widely used for machine learning. Understanding its key features and setup helps leverage its full potential for regression tasks.

## Slide 33: Key features of TensorFlow
Flexible Architecture
  TensorFlow provides a flexible architecture suitable for a wide range of machine learning models and workflows.
Deep Learning Support
  TensorFlow supports deep learning applications, enabling complex neural network designs and training.
Efficient Computation
  TensorFlow efficiently utilizes CPUs and GPUs to accelerate computation for faster training and inference.
Community Support
  TensorFlow benefits from extensive community support, offering resources, tools, and collaboration opportunities.
Notes: --- TensorFlow offers flexible architecture, support for deep learning, efficient computation on CPUs and GPUs, and extensive community support, making it ideal for various machine learning tasks. Image source: Microsoft 365 content library

## Slide 34: Setting up TensorFlow for machine learning
TensorFlow Installation
  Install TensorFlow library using package managers like pip for efficient machine learning workflows.
Environment Configuration
  Configure programming environments such as Python and virtual environments for smooth TensorFlow usage.
Dataset Preparation
  Prepare and preprocess datasets to ensure compatibility and accuracy in regression model training.
Notes: --- Setting up TensorFlow involves installing the library, configuring environments, and preparing datasets. Proper setup ensures smooth implementation of regression models. Image source: Microsoft 365 content library

## Slide 35: Advantages of TensorFlow for regression tasks
Scalable Model Building
  TensorFlow supports scalable construction of regression models suitable for various data sizes and complexities.
Data Pipeline Integration
  TensorFlow easily integrates with diverse data pipelines ensuring smooth data flow for regression tasks.
Robust Training and Evaluation
  TensorFlow offers comprehensive tools for training, evaluation, and optimisation of regression models.
Notes: --- TensorFlow provides scalable model building, easy integration with data pipelines, and robust tools for training and evaluation, facilitating effective regression modelling. Image source: Microsoft 365 content library

## Slide 36: Implementing Regression Models in TensorFlow
Notes: Implementing regression models in TensorFlow involves data preparation, model construction, training, and evaluation. Each step is crucial for building accurate predictive models.

## Slide 37: Preparing data for TensorFlow regression
Data Cleaning
  Removing errors and inconsistencies from data is essential for accurate regression model training.
Data Normalisation
  Normalising data scales values to a common range, improving model convergence and performance.
Training and Testing Split
  Splitting data into training and testing sets helps evaluate model accuracy and avoid overfitting.
Notes: --- Data preparation includes cleaning, normalising, and splitting data into training and testing sets to ensure the model learns effectively without bias. Image source: Microsoft 365 content library

## Slide 38: Building a linear regression model
Model Structure
  Linear regression uses layers to connect input features with output predictions clearly and efficiently.
Weight Optimization
  Weights are adjusted during training to minimise prediction errors and improve model accuracy.
Notes: --- A linear regression model in TensorFlow is built using layers to represent input features and output predictions, with weights optimised during training to minimise errors. Image source: Microsoft 365 content library

## Slide 39: Training, evaluation, and interpretation
Model Training Process
  Training involves feeding data through the model and adjusting its parameters to improve performance.
Evaluation Metrics
  Evaluation metrics like mean squared error measure the model's accuracy and performance.
Model Interpretation
  Interpretation helps understand insights from the model to explain its predictions and behaviour.
Notes: --- Training involves feeding data through the model and adjusting parameters. Evaluation metrics like mean squared error assess performance, while interpretation helps understand model insights. Image source: Microsoft 365 content library

## Slide 40: Advanced Techniques and Best Practices
Notes: Advanced methods such as using neural networks for non-linear regression, preventing overfitting, and effective visualisation enhance regression model accuracy and interpretability.

## Slide 41: Handling non-linear regression with neural networks
Neural Networks Structure
  Neural networks use multiple stacked layers to capture complex non-linear relationships in data.
Activation Functions
  Activation functions introduce non-linearity, enabling neural networks to model varied data patterns beyond linear regression.
Advanced Regression Modeling
  Neural networks extend regression capabilities by effectively handling complex, non-linear data relationships.
Notes: --- Neural networks in TensorFlow can model complex non-linear relationships by stacking layers and using activation functions, expanding regression capabilities beyond linear patterns. Image source: Microsoft 365 content library

## Slide 42: Preventing overfitting and improving model performance
Regularisation Techniques
  Regularisation adds penalty terms to reduce model complexity and prevent overfitting in training.
Dropout Method
  Dropout randomly disables neurons during training to improve model generalisation and reduce overfitting.
Early Stopping Strategy
  Early stopping halts training when validation performance declines, avoiding overfitting on training data.
Notes: --- Techniques like regularisation, dropout, and early stopping help prevent overfitting, ensuring the model generalises well to new data and maintains predictive accuracy. Image source: Microsoft 365 content library

## Slide 43: Visualising and interpreting results
Loss Curves Insight
  Loss curves help track model performance over training, revealing convergence or overfitting trends.
Regression Plot Utility
  Regression plots illustrate relationships between variables, helping interpret model predictions and fit quality.
Residual Analysis Importance
  Residual analysis exposes model errors and biases, supporting diagnosis and improvement.
Notes: --- Visual tools like loss curves, regression plots, and residual analysis aid in understanding model behaviour, diagnosing issues, and communicating results effectively. Image source: Microsoft 365 content library

## Slide 44: Conclusion
Versatile Platform
TensorFlow offers a flexible platform supporting various regression analysis techniques for diverse applications.
Comprehensive Tools
The platform provides comprehensive tools enabling both foundational and advanced regression modelling.
Powerful Predictive Solutions
Applying TensorFlow’s techniques unlocks powerful predictive solutions across multiple domains and industries.
Notes: TensorFlow is a versatile platform that empowers effective regression analysis through comprehensive tools and flexible modelling. Applying foundational and advanced techniques unlocks powerful predictive solutions across domains.