## Slide 1: Predict the fuel burnt (kg)
PRC Data Challenge 2025 -> https://ansperformance.eu/study/data-challenge/dc2025/
October – November 2025
Team details:
Our team name is : understated-zucchini
Our submission bucket is : prc-2025-understated-zucchini

## Slide 2: Main principle
Feed the model with Fuel Flow Kg/Seconds (instead of fuel Kilograms)
Compute the Fuel Flow from Fuel (kg) between Fuel Start Instant and Fuel End Instant
Before submitting the ranking/final results , revert predicted fuel flow
  From fuel flow in Kg/Seconds to fuel consumption in Kg
  Explanation : it is easier to compare delta values and find the dependent variables contribution than it would be with an absolute value (strongly related to a delta time frame, delta between fuel start and fuel end instants

## Slide 3: Data Model
Fuel Data
Flight Data
Flight id
Flight List Data
Airport Data
Aircraft Data
Flight id
origin airport ICAO code
destination airport ICAO code
Aircraft ICAO code
Fuel End vs Flight Timestamp
Fuel Start vs Flight Timestamp
Wind Data
Latitude longitude altitude
timestamp

## Slide 4: Principles
Read Fuel Train records
  compute time difference seconds = fuel record end – fuel record start
  Compute fuel flow kg per seconds = fuel kg / ( fuel record end – fuel record start )
Link to Flight List using the flight id
  Compute fuel burn relative start = fuel burnt start – takeoff (from the related flight list)
  Compute fuel burn relative end = fuel burnt end – takeoff (from the related flight list)
Extend fuel records with attributes coming from the flight list
  Add origin longitude, origin latitude, origin_elevation
  Add destination longitude, destination latitude, destination elevation
  Add flight distance Nautical Miles and flight duration seconds

## Slide 5
Airports

## Slide 6: Airports sanity checks
Ensure that all airports (origin and destination) found in the flight list files are available in the airports database
Solution -> concat list of airports (origin and destination) from all the 3 flight list files, suppress duplicates and ensure that all airports ICAO code are available in the airports database
Ensure that each of these airports, as available in the airports database has latitude, longitude and elevation with valid values
Valid values for latitude and longitude are their nominal ranges
Elevation must be a real number (not a number is an error)

## Slide 7: Airports data sanity checks
Airport ZGOW Jieyang Chaoshan International Airport has a missing “elevation ft”
Status as of

## Slide 8: Airports data sanity checks
Icao code not empty and length > 0
Latitude in the range -90,0 and + 90,0
Longitude in the range -180 and +180,0
Elevation in feet > 0,0 feet
Elevation in feet * feet_to_meters < 5000,0 meters
Notes:
  airport ICAO = ZUDR --> elevation = 14108.0 feet--> elevation = 4300.1184 meters
  airport ICAO = ZX and UPL --> elevation = 13943.0 feet --> elevation = 4249.8264 meters

## Slide 9: airports lat/lon and aircraft lat/lon
Latitude:
Values range from -90° to +90°.
Lines of latitude run east-west and are parallel to each other.
The equator is at 0° latitude.
Longitude:
Values range from -180° to +180°.
Lines of longitude run north-south and converge at the poles.
The prime meridian (0° longitude) runs through Greenwich, England. These ranges define the geographic coordinate system used to specify locations on Earth.

## Slide 10: Airports data sanity checks
airport ICAO = LLMZ --> elevation (feet) = -1266.0 --> elevation meters = -385.8768

## Slide 11
Flight Lists

## Slide 12: Flight list – sanity checks
Assert (takeoff() != null )
Assert (takeoff().getEpochSecond() > 0)
Assert (landed() != null)
Asser (landed().getEpochSecond() > 0)
Assert landed().isAfter(takeoff())
Example for Java code

## Slide 13: Set takeoff and landing date type as UTC Compute flight distance compute flight duration Extract year from takeoff Extract month from takeoff Extract day of the year (1..365) from takeoff Compute distance (great circle using haversine method) between departure and arrival airports compute flight duration between takeoff and landing -> Principles is to get rid of absolute datetime convert lat long into sine and cosine -> favorize model analysis because of discontinuity from -180 degrees to 0 degrees and avoid scaling only absolute degrees
Extend Flight list records

## Slide 14: Extend Flight list records
Suppress airport names
Compute distance (Nautical miles) between departure and arrival airport
Convert all Date Time instant to UTC
Compute flight time between flight takeoff and flight landed
Use time difference for all instant versus flight takeoff
From flight date
  extract year and month
  Compute day number in the current year (range 1 to 365)
Suppress absolute dates as they are replaced by relative ones from takeoff instant

## Slide 15: Check great circle distance (in nautical miles)
origin_icao | origin_name | destination_icao | destination_name | flight_distance_Nautical miles
MMGL | Guadalajara International Airport | KOAK | Oakland International Airport | 1427.58
Oakland
Guadalajara

## Slide 16
Aircrafts

## Slide 17: Aircrafts data
File obtained from FAA site
FAA-Aircraft-Char-DB-AC-150-5300-13B-App-2023-09-07.xlsx
https://www.kaggle.com/datasets/huynhtruc109/aircraft-faa
Contains 2 interesting columns that may be signals / differenciators for the fuel consumption
  Wingspan_ft_without_winglets_sharklets
  Wingspan_ft_with_winglets_sharklets

## Slide 18: Aircrafts features
3 options ->
option one -> use one hot encoder / getDummies to add as much aircraft ICAO codes in both train and rank and use 0 or 1 to encode the aircraft
Option two -> do not use hot encoder / getDummies and provide additional features to characterize the aircraft
  int Num_Engines, float Approach_Speed_knot, float Wingspan_ft_without_winglets_sharklets, float Wingspan_ft_with_winglets_sharklets,
  float Length_ft, float Tail_Height_at_OEW_ft, float Wheelbase_ft, float Cockpit_to_Main_Gear_ft, float Main_Gear_Width_ft,
  // Maximum take off weight -> double MTOW_lb, double MTOW_kg,
  // Maximum landing weight -> double MALW_lb, double MALW_kg,
  float Parking_Area_ft2
Option 3 -> use both

## Slide 19: Aircrafts in rank and final
PRC Aircrafts in Rank and Final
A20N
A21N
A306
A319
A320
A321
A332
A333
A359
B38M
B734
B737
B738
B739
B744
B752
B763
B772
B77L
B77W
B788
B789
Use this list of aircrafts in Rank and Final to reduce the train dataset

## Slide 20
Fuel

## Slide 21: fuel absolute datetime instant
Compute relative duration in seconds from the “flight” takeoff instant
Fuel Start Instant (UTC) – absolute instant (not very useful for the model)
  converted to duration from the “takeoff”UTC Instant
  Converted to duration until the “landed” UTC instant
Fuel End Instant (UTC) – absolute instant (not very useful for the model)
  converted to duration from the “takeoff” UTC Instant
  Converted to duration until the “landed” UTC instant

## Slide 22: Fuel data injected into flight data
In order to prepare for interpolation, fuel start and fuel end of the same flight_id are inserted in the flight data of the same flight_id

## Slide 23
Flights

## Slide 24: flight data files with holes / missing values in latitude, longitude or altitude
There are “hundreds” of Train files with at least one missing value in Latitude, Longitude or Altitude

## Slide 25: Erroneous <<train>> flight data

## Slide 26: Erroneous <<train>> flight data

## Slide 27: Erroneous <<train>> flight data

## Slide 28: Feature engineering heading-track-and-radial
Heading. The direction in which the longitudinal axis of an aircraft is pointed, usually expressed in degrees from North (true, magnetic, compass or grid). (Source: ICAO)
Track. The projection on the earth’s surface of the path of an aircraft, the direction of which path at any point is usually expressed in degrees from North (true, magnetic or grid). (Source: ICAO)
Radial. A magnetic bearing extending from a VOR/VORTAC/TACAN. (Source: UK CAA)
Bearing. The horizontal direction to or from any point, usually measured clockwise from true north, magnetic north, or some other reference point through 360 degrees. (Source: US FAA)

## Slide 29: Feature engineering of track angles
The track angle is given in Decimal degrees
Angles in the range 0 degrees to 360 degrees are not good inputs to the models
Because 360° et 0° must be near and avoid discontinuity when moving from 360 degrees to 0 degrees.
To avoid discontinuity
Compute sinus and cosinus of each angles
In radians before feeding the model
During interpolation use modulo 360…
For the track angle compute a vector
from the ground speed

## Slide 30: Combine ground speed and track angle
Mais la donnée « aircraft track angle » sera plus facile à interpréter pour le modèle si vous convertissez les colonnes de direction et de vitesse de l’avion en un vecteur vitesse
import numpy as np
''' convert track angles from degrees to radians '''
track_radians = df.pop('track')* np.pi / 180
groundSpeedMax = df['groundspeed'].max()
groundSpeed = df.pop('groundspeed')
# Calculate the aircraft speed x and y components.
df['groundspeed_x'] = groundSpeed * np.cos(track_radians)
df['groundspeed_y'] = groundSpeed * np.sin(track_radians)

## Slide 31: aircraft flight position at fuel start and fuel end
Compute each aircraft interpolated position at fuel start and fuel end
Use Latitude Longitude of interpolated aircraft position to compute
  For each fuel start Instant compute
    Haversine distance Nm from aircraft position to departure/origin airport
    Haversine distance Nm from aircraft position to arrival/destination airport
  For each fuel end Instant compute
    Haversine distance Nm from aircraft position to departure/origin airport
    Haversine distance Nm from aircraft position to arrival/destination airport

## Slide 32: Flight data cleaning
Example -> training flight prc770822360 contains duplicated timestamps
org.apache.commons.math3.exception.NonMonotonicSequenceException: les points 12 et 13 ne sont pas strictement croissants (1 744 474 640 >= 1 744 474 640)

## Slide 33: Interpolation -> Groundspeed
Due to insertion of takeoff “pseudo” series
Due to insertion of landed “pseudo” series

## Slide 34: Interpolation -> track angle
Consequences of insertion of heading angle from origin to destination
At takeoff and at landed (first and last timestamp in augmented flight data
Track angles must be constrained using modulo 360,0 degrees

## Slide 35: Interpolation -> vertical rate

## Slide 36
Training versus Validation loss

## Slide 37: Training versus Validation loss
16 october 2025
Y = fuel flow kg per seconds
Make the val_loss as low as possible
All train records
133984 train fuel records
11085 train flight files

## Slide 38: Do not
You do not need to scale the Y of train data as the algorithm or model will set the parameter values to get least Cost (error), that is k {Y (output)-Y (original)} anyway.

## Slide 39: 25 October 2025
Input to the modeling
Train-> ['time_diff_seconds', 'fuel_flow_kg_sec', 'aircraft_latitude_at_fuel_start', 'aircraft_longitude_at_fuel_start', 'aircraft_latitude_at_fuel_end', 'aircraft_longitude_at_fuel_end', 'aircraft_distance_flown_Nm', 'aircraft_altitude_ft_at_fuel_start', 'aircraft_altitude_ft_at_fuel_end', 'aircraft_computed_vertical_rate_ft_min', 'aircraft_groundspeed_kt_at_fuel_start', 'aircraft_groundspeed_kt_at_fuel_end', 'aircraft_track_angle_deg_at_fuel_start', 'aircraft_track_angle_deg_at_fuel_end', 'aircraft_vertical_rate_ft_min_at_fuel_start', 'aircraft_vertical_rate_ft_min_at_fuel_end', 'origin_elevation_feet', 'destination_elevation_feet', 'flight_distance_Nm', 'flight_duration_sec’]
Rank -> ['time_diff_seconds', 'aircraft_latitude_at_fuel_start', 'aircraft_longitude_at_fuel_start', 'aircraft_latitude_at_fuel_end', 'aircraft_longitude_at_fuel_end', 'aircraft_distance_flown_Nm', 'aircraft_altitude_ft_at_fuel_start', 'aircraft_altitude_ft_at_fuel_end', 'aircraft_computed_vertical_rate_ft_min', 'aircraft_groundspeed_kt_at_fuel_start', 'aircraft_groundspeed_kt_at_fuel_end', 'aircraft_track_angle_deg_at_fuel_start', 'aircraft_track_angle_deg_at_fuel_end', 'aircraft_vertical_rate_ft_min_at_fuel_start', 'aircraft_vertical_rate_ft_min_at_fuel_end', 'origin_elevation_feet', 'destination_elevation_feet', 'flight_distance_Nm', 'flight_duration_sec']

## Slide 40: missing
Date of the flight -> year, month, day in the year
Fuel burn relative start to takeoff
Fuel burn relative end to takeoff
Fuel burn relative end to landed
Mach
CAS
TAS
Aircrafts data

## Slide 41: steps
Read fuel records
Extend each fuel record with flight data
Scale and encode aircraft icao code
Read Flight list records
Extend fuel records with flight list data
Y column is fuel flow kg per seconds
Use fuel start end relative stamp to link with flight record timestamp
Timestamp inside start – end of fuel record
Compute fuel flow kg per seconds
Compute flight distance (Nm)
Compute flight duration (seconds)
Encode aircraft_icao_code
Scale all columns

## Slide 42: Flight file with issues
Parquet file <<C:\Users\rober\git\PRCdataChallenge2025\Data-Download-OpenSkyNetwork\competition-rank-data\prc806717600.parquet>

## Slide 43: Fundamental concepts of regression
Definition of Regression
  Regression estimates relationships between dependent and independent variables to understand their connection.
Predicting Continuous Outcomes
  The goal of regression is to predict continuous variables based on input data from other variables.
Understanding Variable Influence
  Regression helps identify how independent variables influence the dependent variable in a measurable way.
Notes: --- Regression involves estimating the relationship between dependent and independent variables. We aim to predict continuous outcomes and understand how variables influence each other. Image source: Microsoft 365 content library

## Slide 44: Types of regression problems
Linear Regression
  Linear regression models the relationship between variables using a straight line for simple, direct trends.
Polynomial Regression
  Polynomial regression handles complex data by fitting a curved line to capture non-linear relationships.
Logistic Regression
  Logistic regression models probabilities for classification problems using an S-shaped logistic curve.
Notes: --- Common regression types include linear, polynomial, and logistic regression. Each type addresses different data patterns and modelling needs, from simple linear relationships to complex non-linear dependencies. Image source: Microsoft 365 content library

## Slide 45: Advantages of TensorFlow for regression tasks
Scalable Model Building
  TensorFlow supports scalable construction of regression models suitable for various data sizes and complexities.
Data Pipeline Integration
  TensorFlow easily integrates with diverse data pipelines ensuring smooth data flow for regression tasks.
Robust Training and Evaluation
  TensorFlow offers comprehensive tools for training, evaluation, and optimisation of regression models.
Notes: --- TensorFlow provides scalable model building, easy integration with data pipelines, and robust tools for training and evaluation, facilitating effective regression modelling. Image source: Microsoft 365 content library

## Slide 46: Preparing data for TensorFlow regression
Data Cleaning
  Removing errors and inconsistencies from data is essential for accurate regression model training.
Data Normalisation
  Normalising data scales values to a common range, improving model convergence and performance.
Training and Testing Split
  Splitting data into training and testing sets helps evaluate model accuracy and avoid overfitting.
Notes: --- Data preparation includes cleaning, normalising, and splitting data into training and testing sets to ensure the model learns effectively without bias. Image source: Microsoft 365 content library

## Slide 47: Building a linear regression model
Model Structure
  Linear regression uses layers to connect input features with output predictions clearly and efficiently.
Weight Optimization
  Weights are adjusted during training to minimise prediction errors and improve model accuracy.
Notes: --- A linear regression model in TensorFlow is built using layers to represent input features and output predictions, with weights optimised during training to minimise errors. Image source: Microsoft 365 content library

## Slide 48: Training, evaluation, and interpretation
Model Training Process
  Training involves feeding data through the model and adjusting its parameters to improve performance.
Evaluation Metrics
  Evaluation metrics like mean squared error measure the model's accuracy and performance.
Model Interpretation
  Interpretation helps understand insights from the model to explain its predictions and behaviour.
Notes: --- Training involves feeding data through the model and adjusting parameters. Evaluation metrics like mean squared error assess performance, while interpretation helps understand model insights. Image source: Microsoft 365 content library

## Slide 49: Handling non-linear regression with neural networks
Neural Networks Structure
  Neural networks use multiple stacked layers to capture complex non-linear relationships in data.
Activation Functions
  Activation functions introduce non-linearity, enabling neural networks to model varied data patterns beyond linear regression.
Advanced Regression Modeling
  Neural networks extend regression capabilities by effectively handling complex, non-linear data relationships.
Notes: --- Neural networks in TensorFlow can model complex non-linear relationships by stacking layers and using activation functions, expanding regression capabilities beyond linear patterns. Image source: Microsoft 365 content library

## Slide 50: Preventing overfitting and improving model performance
Regularisation Techniques
  Regularisation adds penalty terms to reduce model complexity and prevent overfitting in training.
Dropout Method
  Dropout randomly disables neurons during training to improve model generalisation and reduce overfitting.
Early Stopping Strategy
  Early stopping halts training when validation performance declines, avoiding overfitting on training data.
Notes: --- Techniques like regularisation, dropout, and early stopping help prevent overfitting, ensuring the model generalises well to new data and maintains predictive accuracy. Image source: Microsoft 365 content library

## Slide 51: Visualising and interpreting results
Loss Curves Insight
  Loss curves help track model performance over training, revealing convergence or overfitting trends.
Regression Plot Utility
  Regression plots illustrate relationships between variables, helping interpret model predictions and fit quality.
Residual Analysis Importance
  Residual analysis exposes model errors and biases, supporting diagnosis and improvement.
Notes: --- Visual tools like loss curves, regression plots, and residual analysis aid in understanding model behaviour, diagnosing issues, and communicating results effectively. Image source: Microsoft 365 content library

## Slide 52: Conclusion
Versatile Platform
TensorFlow offers a flexible platform supporting various regression analysis techniques for diverse applications.
Comprehensive Tools
The platform provides comprehensive tools enabling both foundational and advanced regression modelling.
Powerful Predictive Solutions
Applying TensorFlow’s techniques unlocks powerful predictive solutions across multiple domains and industries.
Notes: TensorFlow is a versatile platform that empowers effective regression analysis through comprehensive tools and flexible modelling. Applying foundational and advanced techniques unlocks powerful predictive solutions across domains.